## Slide 1: Annual Mining Conference Victoria Falls 1 June 2023 Eng. H. CHOGA ZETDC MANAGING DIERCTOR (A)

## Slide 2: History of the Zimbabwe Power System
The grid started around 1960 with commissioning of the Kariba dam and the 330kV CAPCo network
Hwange power station was built in the 1980s
It has developed to a 2000MW network over the past 60 years

## Slide 3: Current Demand and Supply Situation
Source | Installed Capacity | Current Capacity | Comment
 | (MW) | (MW) | 
Kariba | 1050 | 424MW | Yearly average capacity limited to 424MW by low Lake level. Winter average capacity is 562MW
Hwange I&II | 920 | 225 | Performance generally poor against a planned target of 290MW - 450MW.
Hwange III | 600 | 300 | The 2 generators are under commissioning tests
 |  |  | Coal supply erratic and breakdowns frequent.
Small Thermals | 300 | 0 - 30 | Supply generally ranging from 0MW – 30MW against planned capacity of 45MW.
IPPs | 109.85 | 51-109.85 | Affected by seasonal water levels.
HCB | 50 | 50 | 50MW Firm
Eskom | 400 | 70-100 | 100MW Firm & 350MW Non-Firm at 50% load factor. Supply affected when SA gets to load shedding thus the firm supply can go down to 70MW
EDM | 200 | 10 | 50MW firm and 150MW non firm, currently getting 10MW, awaiting ZETDC clearance of outstanding debt
ZESCO | 150 | 50 | Contract resumption awaiting ZETDC prepayment of month ahead energy requirements. Currently Zesco is supplying 50MW
DAM | 100 | 0 -100 | Depends on funding and power availability in market.
N-Power | -80 | -80 | Anchoring the ZPC Kariba Extension loan amortization.
TOTAL | 3800 | 1000-1319 | 
DEMAND | - | 1155 -1900 | 
Deficit/Surplus | - | 0 – 581 | Load shedding currently implemented

## Slide 4: Committed Power Plants
Plant | Installed capacity (MW) | Fuel | Planned entry into operation
Hwange 7 | 300 | Coal | Under commissioning
Hwange 8 | 300 | Coal | Under commissioning
Great Zimbabwe | 5 | Water (Small HPP) | 2023
Tugwi Mukosi | 15 | Water (Small HPP) | 2024
Gwayi Shangani | 10 | Water (Small HPP) | 2024
Hwange repowering | 300 | Coal | 2026

## Slide 5: Candidate Power Plants
Plant | Installed capacity (MW) | Fuel | Available from year
Batoka Gorge | 1,200 | Hydro | 2032
Devil’s Gorge | 620 | Hydro | 2035
Zhongxin 2 | 270 | Coal | 2025
Thuli Coal | 600 | Coal | 2027
Gokwe North | 1,400 | Coal | 2028

## Slide 6: Future load growth
2300MW within NDS1
  Mining loads mainly
  305k households ready for connection

## Slide 7: Challenges for the power sector
Non cost reflective tariff
  Confirmed by an independent study which was commissioned by gvt.
Antiquated equipment
Maintenance and refurbishment backlog
Skills flight
Inadequate power supply
Forex shortage for power imports
Climate change

## Slide 8: Proposed solutions for mining industry
Install solar plant for own consumption
  Bank excess in the grid through net metering
  Withdraw energy during the night
  Enter into balancing agreement with Zesa
Use IEUG for power supply
Direct imports

## Slide 9: The End
Thank You